## Slide 1: “Projet S5”

## Slide 2: Sommaire
État de l’art
  Angle d’arrivée
  Wifi vs LoRa vs BT
  BT vs BLE
  Avantages de BLE
Problématique
  Chantier 3.0
  Titre du « Projet S5 »
Solution
  « BLE Advertisement Mode »
  Beacon
    Fonctionnement
    Format
    …
  Caractérisations de la carte
  Calendrier

## Slide 3: Angle d’arrivée
Notes: In the angle of arrival (AoA) method, the device to which direction is being determined, such as a tag in an RTLS solution, transmits a special direction finding signal using a single antenna. The receiving device, such as a locator in that same RTLS solution, has multiple antennae arranged in an array. As the transmitted signal crosses the array, the receiving device sees a signal phase difference due to the difference in distance from each of the antenna in its array to the transmitting antenna. The receiving device takes IQ samples of the signal while switching between the active antenna in the array. Based on the IQ sample data, the receiving device can calculate the relative signal direction. The AoA method of direction finding is intended for use with RTLS as well as proximity solutions, such as item finding and point of interest (PoI) information services.
Angle of Arrival (AoA)
Angle of Arrival (AoA) based approaches use antennae arrays [22] (at the receiver side) to estimate the angle at which the transmitted signal impinges on the receiver by exploiting and calculating the time difference of arrival at individual elements of the antennae array. The main advantage of AoA is that the device/user location can be estimated with as low as two monitors in a 2D environment, or three monitors in a 3D environment respectively.
it requires more complex hardware and careful calibration compared to RSS techniques, while its accuracy deteriorates with increase in the transmitter-receiver distance where a slight error in the angle of arrival calculation is translated into a huge error in the actual location estimation [21]. Moreover, due to multipath effects in indoor environments the AoA in terms of line of sight (LOS) is often hard to obtain. Figure 2 shows how AoA can be used to estimate the user location (as the angles at which the signals are received by the antenna array can help locate the user device.).

## Slide 4: Wifi vs LoRa vs BT
Tableau page 10 (Wifi, LoRa et BT)
+ info des doc pour nous
Notes: Most of the current smart phones, laptops and other portable user devices are WiFi enabled, which makes WiFi an ideal candidate for indoor localization and one of the most widely studied localization technologies in the literature. Since existing WiFi access points can be also used as reference points for signal collection [21], basic localization systems (that can achieve reasonable localization accuracy) can be built without the need for additional infrastructure.
ToF and AoA techniques can be used to provide WiFi based localization services.
For detailed information about WiFi, readers are referred to [58]
Bluetooth Low Energy (BLE), also known as Bluetooth Smart, can provide an improved data rate of 24Mbps and coverage range of 70-100 meters with higher energy efficiency, as compared to older versions [9]. While BLE can be used with different localization techniques such as RSSI, AoA, and ToF, most of the existing BLE based localization solutions rely on RSS based inputs as RSS based sytems are less complex.
two BLE based protocols, i.e., iBeacons (by Apple Inc.) and Eddystone (by Google Inc.), have been recently proposed, primarily for context aware proximity based services.
The protocol allows a BLE enabled device (also known as iBeacon or beacon) to transmit beacons or signals at periodic interval. The beacon message consists of a mandatory 16 byte Universally Unique Identifier (UUID)4 and optional 2 byte major5 and minor values6.
Based on the strength of the RSSI, the user is classified in immediate (<1m), near (1- 3m), far (>3m) and unknown regions.
A fundamental constraint of iBeacons (imposed by Apple) is that only the average RSSI value is reported to the user device every one second, even though the beacons are transmitted at 50 ms intervals.

## Slide 5: BT vs BLE
Intro to BT doc page 15 tableau
Notes: BT vs BLE
https://www.sciencedirect.com/topics/computer-science/piconets

## Slide 6: Avantages de BT
Intro to BT doc page 17